## Slide 1: Dreptul la Incalzire
Dragostin Catalin

## Slide 2: CALDURA : UNDE SUNTEM ASTAZI ? SITUATIA INCALZIRII CENTRALIZATE DIN ROMANIA Sursa: COGEN-Romania, 2010
DE CE SA REGLEMENTEZE O INVESTITIE CARE REDUCE COSTURILE ? EPC >20%

## Slide 3: UNDE SUNTEM ? POTENTIALUL RES IN ROMANIA Sursa: Icemenerg, NRAP
(mii TEP)

## Slide 4: CE AM REALIZAT DIN RES ?!

## Slide 5: CALDURA: UNDE SUNTEM ASTAZI ? Deja se foloseste “dezordonat” ~40% incalzire pe lemne ! (potential COGEN )
Chart: COMBUSTIBILI FOLOSITI DE POPULATIE (1996)
| Lemne de foc | Gaz natural | Energie termica | Energie electrica | GPL | TOTAL
(mii tep) | 4739.9604 | 2261.4284 | 1158.3222 | 972.6822 | 412.7396 | 9545.1328

## Slide 6: DATE STATISTICE INS CONSUM LEMN DE FOC (Preponderent Biomasa Forestiera)
INCALZIRE
3,5 mil.locuinte
~9,5 mil.tone “ilegal”
~10 mil.tone “legal”

## Slide 7: INTERPRETAREA ENERGETICA A DATELOR INS DPDV “STRATEGIC”
19,5 mil.tone/an biomasa = ~66,3 mil.MWh/an
La o durata minim economica de 5000 h/an functionare, potentialul energetic de micro/medie-cogenerare distribuita pentru incalzire ar fi :
  ~13.000 MW, din care :
    ~10,000 MWh putere termica utila transformabila in caldura si electricitate astfel:
      ~2500 MWe
      ~7500 MWt
Consideram numai ~30% potential tehnic si economic realizabil
  ~800 MWe (1 grup nuclear de la CNE Cernavoda !);
  ~2300 MWt, capacitate de incalzire a majoritatii oraselor mari/medii din Romania

## Slide 8: Quote from: www.res4less.eu
Romania are un SURPLUS (!) de potential productie numai de electricitate din biomasa de 6,4 TWh/an (~1 grup nuclear ca Cernavoda !)
  Surplus de “potential ESRE”: ce ramine dupa indeplinirea obligatiei ESRE a statului respectiv
  Exista SM interesate sa investeasca in acest potential, in contul obligatiei proprii
Riscuri identificate:
  Acceptarea politica;
  Accesul la resurse (biomasa)

## Slide 9: SPRE CE TREBUIE SA NE INDREPTAM ? (Dir. 27/2012)

## Slide 10: ?
Nimeni nu pomeneste, nici macar CE, despre incalzirea “din nimic” (adica Vint !)
if we need heat, should we always burn something !?
Avem in Romania ~4000 MW despre care ne vaitam ca “cer certificate verzi” si, cind bate vintul, e “prea multa energie”

## Slide 11: CHP “BATTERY” -warm up with cold wind- (if we need heat, should we always burn something !?) Presented at: “2nd German‐Japanese Workshop on Renewable Energies” 5‐7 July 2017, Stuttgart, Germany
Dragostin Catalin – Director, SC ENERGY SERV SRL
- President, ESCOROM
Patent application, Legal Assistance: Law firm Ciurtin & Associates

## Slide 12: Possible Configuration Arrangements (to meet the GC- Green Certificates- regulations)
2 GC
Heat Pipe<10 Km
Dedicated Transp. Line>10 Km
Specific Cost ~0,1 mill.EUR/Km
2 GC
2 GC
OPTION 1
OPTION 2

## Slide 13: CONCLUSIONS
District Heating of Constanta, Navodari, Mangalia, Braila and Galati provide the highest levels of “sink energy” for balancing purposes, due to high penetration level of wind energy in Dobrogea;
For each city, some energy wind operators may “associate” to supply power for CHP generation;
Probably, the most cost effective way could be a dedicated power transmission line, which may be a cheap option for 3-4 operators, for a distance of max. 20-30 Km (max. 3 mill.EUR)
In the future, probably the wind farm planners may consider the heat supply options and not only electricity, for improving the operation efficiency and economics

## Slide 14: Multumesc !
Energy Serv SRL, Bucuresti
Tel: 021-311-8345
Fax: 021-319-3214
Email: office@energy-serv.ro
catalin.dragostin@energy-serv.ro
Mobile: 0040-744-569-150